## Slide 1: MCU TNC Deliverable 4
David Cain, Kobe Keopraseuth, and Kaleb Leon

## Slide 2: Project Introduction
What is a TNC
  A modem for connecting a computer with a HAM radio
  KISS
  AX.25
Why are we designing a TNC
  Our design is a starting point for further development to be completed by the C.A.P.E. program
  Thorough documentation
TNC
TNC
Diagram of TNC use

## Slide 3: Technical Details
KISS
  Packet structure used to get information from computer into TNC
AX.25
  Packet structure used when output audio waveform for radio to transmit
AFSK
  Frequency encoding scheme used to represent data bitstream
  Bi-modal frequency representation
AX.25 Packet Structure

## Slide 4: Current Progress
Code
  Transmission
    Using onboard DAC, an AFSK waveform is output
    Baud rate is controlled by a timer interrupt for high precision
  Receiving
    Default mode until signaled to transmit
    Count frequencies coming from radio by using external interrupt
Hardware
  Transmission
    MOSFET controls PTT line from radio
    LED indicate transmission status
  Receiving
    BJT voltage amplifier circuit tuned to trigger hardware interrupt on controller
    Output is filter with Low-Pass Filter
    LED indicates Receiving status

## Slide 5: Remaining Effort
• Finish receiving logic
  CRC calculation
  Add more packet fault detection
  NRZI Encoding detection
• Finish transmission logic
  AFSK waveform currently has voltage blips from software
  Add hardware for scaling down a 3.3V ptp AFSK signal
  NRZI Encoding